## Slide 1
PROJECT BASED LEARNING • EMBEDDED SYSTEMS
SMART INDUSTRIAL SAFETY CONTROL
A microcontroller-based safety monitoring and control prototype
SENSE
DECIDE
ACT
Koneru Lakshmaiah Education Foundation

## Slide 2
Project at a glance
OVERVIEW
02
A compact embedded control concept that monitors an input condition and supports safety-state handling.
01 SENSE
An IR sensor provides a digital input representing a detected condition.
02 DECIDE
Firmware defines NORMAL, WARNING and EMERGENCY safety states.
03 CONTROL
GPIO outputs, an LED, relay/motor-control signals and timer peripherals support the response.
Implementation basis: STM32CubeIDE project • STM32 HAL • C firmware
Important: this is a prototype foundation, not a certified industrial safety system.

## Slide 3
Problem statement & motivation
CONTEXT
03
Industrial work areas can expose people and equipment to moving machinery, restricted zones and unexpected events.
Delayed response
If a hazard is noticed only by a person, reaction time can vary.
Limited visibility
Operators may not continuously observe every machine or work zone.
Need for interlocks
A control signal can help indicate a hazard and initiate a safer machine state.
Project question
How can a low-cost microcontroller prototype read a sensor input and organize outputs around explicit safety states?

## Slide 4
Objectives & scope
PLANNING
04
• Build an embedded firmware foundation on the STM32 platform.
• Initialize GPIO and timer peripherals using the STM32 Hardware Abstraction Layer (HAL).
• Represent system condition using NORMAL, WARNING and EMERGENCY states.
• Enable a PWM output and a timer interrupt as part of the peripheral setup.
• Structure the design so sensors and outputs can be extended in later iterations.
In scope
Embedded control logic, sensor input concept, indicators and actuator-control outputs.
Out of scope
Certified machinery protection, validated hazard analysis, production deployment and measured reliability claims.
The scope describes a learning prototype; final behavior must be verified on hardware.

## Slide 5
System architecture
DESIGN
05
IR SENSOR
Digital input
STM32F103RB
GPIO + firmware
SAFETY STATE
Normal / warning / emergency
OUTPUTS
LED / relay
MOTOR CONTROL
PWM-capable path
TIM2
PWM started on Channel 1; configured pulse starts at 0.
TIM4
Base timer started with interrupt enabled.
TIM3
Input-capture peripheral initialized.
The diagram separates the conceptual safety path from the specific timer setup found in the firmware.

## Slide 6
Hardware & peripheral building blocks
IMPLEMENTATION
06
STM32 microcontroller
Executes C firmware and coordinates inputs, states and outputs.
IR sensor
Provides a digital sensing signal; exact range and target depend on the module.
LED / status indicator
Provides a simple local indication when wired and mapped to firmware.
Relay interface
Can switch a separate load through a suitable driver and isolation stage.
Motor-control path
PWM is initialized; power-stage design and safe shutdown require hardware validation.
Timer peripherals
TIM2 PWM, TIM3 input capture initialization, and TIM4 interrupt-based timing.
Electrical design reminder: use appropriate driver circuitry, protection, grounding and isolation. Never drive industrial loads directly from MCU pins.

## Slide 7
Firmware structure
IMPLEMENTATION
07
1 Startup
HAL_Init() and system clock setup.
2 Peripheral init
GPIO, TIM2, TIM3 and TIM4 are initialized.
3 Enable services
TIM2 PWM starts; TIM4 interrupt is enabled and its base timer starts.
Main loop
The while(1) loop is present but contains no application logic in the supplied main.c.
Safety function
Safety_State_Update() is declared, but a definition/call is not visible in the supplied main.c.
This distinction matters: peripheral setup is implemented, but complete sensor-to-state-to-actuator behavior is not demonstrated by the provided main file.

## Slide 8
Three-state safety model
CONTROL LOGIC
08
NORMAL
No hazard condition indicated Expected: normal operation
WARNING
Abnormal condition detected Expected: alert / prepare to stop
EMERGENCY
Critical condition or E-stop Expected: move to safe state
Conceptual return to NORMAL only after the hazard is cleared and an intentional reset is allowed.
Code evidence: SafetyState enum defines NORMAL, WARNING and EMERGENCY; the actual transition rules still need implementation and verification.

## Slide 9
Timer configuration in the source
IMPLEMENTATION DETAIL
09
Peripheral
Configuration visible in main.c
Purpose / interpretation
TIM2
Prescaler 71; Period 999; PWM Channel 1; Pulse 0
PWM output initialized and started
TIM3
Prescaler 7; Period 65535; input-capture init
Capture peripheral setup is present
TIM4
Base timer started with interrupt
Periodic callback path can be used for timing/state checks
Exact output frequency depends on the effective timer clock and prescaler/period settings. Verify the board clock tree and pin mapping before quoting a frequency.

## Slide 10
Intended operating sequence
SYSTEM BEHAVIOR
10
01 Power up
Initialize MCU, clock and peripherals.
02 Read input
Sample the sensor and emergency control input.
03 Evaluate
Apply defined thresholds and priority rules.
04 Signal state
Update indicator and state representation.
05 Control output
Command the actuator interface to a safe condition.
06 Recover safely
Require hazard clearance and deliberate reset.
This sequence is the recommended application workflow. It is not a claim that all six steps are currently implemented in the submitted firmware.

## Slide 11
Verification plan & test cases
TESTING
11
ID
Scenario
Expected behavior
Verification method
T1
Power-on
MCU boots and initializes all configured peripherals
Record startup / debugger evidence
T2
Sensor active
Input level is read consistently
Check GPIO polarity and debounce
T3
Emergency button
Emergency condition overrides normal operation
Verify hardware path and response
T4
Indicator output
Status changes with the defined state
Measure GPIO and observe LED
T5
PWM output
TIM2 Channel 1 output is present as configured
Scope/logic analyzer at mapped pin
T6
Timer interrupt
TIM4 callback executes at expected interval
Toggle test pin or inspect debugger
Results should be filled only after executing each test on the target board. No measured pass/fail data was supplied with the project files.

## Slide 12
Implementation status: what is and isn't shown
STATUS
12
Visible in supplied source
• SafetyState enum • HAL and clock initialization • GPIO and TIM2/TIM3/TIM4 init calls • TIM2 PWM start • TIM4 interrupt enable + base timer start
Needs completion / proof
• Implement and call state-update logic • Confirm sensor and emergency input pin mapping • Connect outputs to transitions • Validate safe-state behavior on hardware • Add measured timing and test evidence
Reported outcome
The project provides a structured embedded starting point for industrial safety control. Performance, response time and reliability must be established through documented testing.
Do not present simulated or planned outcomes as measured experimental results.

## Slide 13
Safety engineering considerations
RISK & RELIABILITY
13
Fail-safe output
Define what happens on reset, sensor disconnect, MCU lockup and power loss.
Emergency stop
Use a suitable hardwired safety circuit where required; do not rely only on application firmware.
Electrical protection
Use rated drivers, flyback protection, isolation and appropriate power separation.
Input robustness
Debounce switches, validate signal polarity, handle noise and detect wiring faults.
Independent testing
Test normal, warning, emergency and fault-injection conditions.
Standards & review
Assess applicable machinery/electrical safety standards with qualified personnel before deployment.
This student prototype must not be used as the sole protective system for real industrial machinery.

## Slide 14
Limitations & future enhancements
ROADMAP
14
Current limitations
• Application loop is empty in supplied main.c • State-update routine is declared but not shown as implemented • No logged hardware test results or measured metrics provided
Next development steps
• Complete sensor polling / interrupt handling • Implement priority-based state transitions • Add watchdog and fault detection • Log events and timestamps • Test output shutdown and recovery
Longer-term extensions
• Add industrial-grade sensors for temperature, gas, vibration or access monitoring.
• Introduce an HMI/dashboard and event history where appropriate.
• Add communications only after defining cybersecurity and fail-safe behavior.
• Perform formal risk assessment, validation and maintenance planning.

## Slide 15
Conclusion & references
WRAP-UP
15
Key takeaways
• The project explores a microcontroller-based approach to industrial safety monitoring.
• The firmware defines three safety states and initializes multiple STM32 timer peripherals.
• The next milestone is to connect sensor inputs, state transitions and outputs, then verify behavior on hardware.
• Safety-critical deployment requires independent protective design and formal validation.
Reference basis
• Project source: Src/main.c and STM32CubeIDE configuration (.ioc) • STMicroelectronics, STM32F1 HAL and reference documentation • IEC 60204-1: Safety of machinery — Electrical equipment of machines (consult current applicable edition) • ISO 13850: Safety of machinery — Emergency stop function (consult current applicable edition)
THANK YOU
Questions & discussion